## Slide 1: SOCKET COMMUNICATION
Prepared by Vishnu C
Date: July 2025

## Slide 2: Overview & Objectives
- Understand TCP socket operations using AT commands on Cavli CQ20
- Learn how to open TCP sockets with AT+QIOPEN
- Learn how to send data with AT+QISEND
- Practice typical command sequences

## Slide 3: CQ20 Module Quick Specs
- LTE Cat 4 module with 2G fallback
- GNSS, VoLTE, and integrated eSIM
- Uses Quectel-based AT command set
- Compatible with AT+QIOPEN and AT+QISEND

## Slide 4: AT+QIOPEN – Open TCP Socket
AT+QIOPEN=<ctx>,<id>,"TCP","<IP>",<port>[,<local_port>,<mode>]
- contextID: PDP context (e.g., 1)
- connectID: 0-11
- access_mode: 0=buffer, 1=push, 2=transparent
URC: +QIOPEN: <id>,<err>

## Slide 5: Access Modes Explained
- Buffer Mode (0): Host polls with AT+QIRD
- Direct Push Mode (1): Auto data URC
- Transparent Mode (2): Acts like serial pipe
- Choose based on streaming vs polling

## Slide 6: AT+QISEND – Sending Data
AT+QISEND=<connectID>[,<length>]
- Prompts with ">" for data entry
- End data with Ctrl+Z
- Response: SEND OK or FAIL
- Supports variable or fixed-length send

## Slide 7: Full TCP Command Example
AT+QICSGP=1,"APN"
AT+QIACT=1
AT+QIOPEN=1,0,"TCP","203.0.113.10",5000,0,0
AT+QISEND=0,11 → Hello world
AT+QISEND=0,0
AT+QICLOSE=0
AT+QIDEACT=1

## Slide 8: Tips & Best Practices
- Ensure PDP is activated (AT+QIACT)
- Monitor +QIOPEN and QISEND URCs
- Use AT+QIGETERROR on failure
- Avoid large sends; split if needed
- Use +++ to exit transparent mode

## Slide 9: Common Errors & Solutions
- SEND FAIL: buffer full → retry
- ERROR: wrong connectID or PDP inactive
- No URC: check timeout or socket error
- Use AT+QIGETERROR for last error

## Slide 10: Summary
- AT+QIOPEN opens TCP connections on Cavli CQ20
- AT+QISEND transmits payloads via socket
- Modes: buffer, push, transparent
- Use correct sequence and monitor URCs

## Slide 11: References
- Cavli CQ20 datasheet
- Quectel UC20 TCP/IP AT Manual
- M2M Support Docs on AT+QISEND
- Quectel Application Notes